## Slide 1: 2D RANS Simulation of an Axisymmetric Turbulent Round Jet
AERO0004 : Turbulent Flows
2025 - 2026
Tom BEAUVE
Guillaume VAILLOT
1
Image adapted from: M. Oberlack, 2022 [1]

## Slide 2: Problem description & geometry
2
Velocity
Inlet
Pressure
Outlet
Latteral inlet
a) Turbulent tube inlet
b) Study domain
3D DNS Reference setup
Re = 3500
D = 0.2 m

## Slide 3: CFD modelling strategy
3
Ansys Fluent
implementation
Symetry
Neumann p
Dirichlet elliptic U
Dirichlet p
2D RANS CFD Model
Domain and boundary readapted
Multibloc structured mesh with quadrilateral elements
Critical backflow

## Slide 4: Convergence / Verification process
4
k-ϵ and k-ω RANS models
1 - Residuals Convergence
3 - Grid size convergence
4 - Boundary turbulence sensitivity
≈ 99k cells
2.25 Scalling
2 - Domain size
convergence
Tolerance

## Slide 5: Results : Self-Similarity
5
: all normalized quantities collapse on one curve
Only functions of
Self-similarity captured by RANS models

## Slide 6: Results : The Round Jet Anomaly
How it fails : Spreading Rate and Velocity Decay
1/5
1/4.1
1/3
6
0.089
0.123
0.117
Spreading rate overestimated by 30 - 40 %
Decay constant underestimated by 20 - 40 %

## Slide 7
The Mechanism of the Anomaly
Reynolds Shear Stress and Eddy Viscosity
7
Reynolds shear stress drives mixing with ambient fluid
overestimated
Excessive mixing
=
Spreading & velocity decay

## Slide 8
Why it Fails: Vortex Stretching
Dissipation Deficit
Source: Kercher et al., IEEE Trans. Comp. Packag. Technol., 2003
8
Jet Spreading
Vortex Stretching
Standard LEVM
Do not sense stretching
Round Jet Anomaly

## Slide 9
Why it Fails: Turbulence Anisotropy
Limitations of the Boussinesq Hypothesis
x1.2
x1.4
x1.2
9
Jet turbulence is strongly anisotropic
Boussinesq hyp.
Single scalar
Unphysical isotropic turbulence forced
Bad Reynolds stress distribution

## Slide 10: Conclusion
Summary: RANS models are qualitatively good but quantitatively inaccurate. Large overprediction of jet spreading for both models
Future Work: Use Pope* correction term in –equation for vortex stretching, Reynolds Stress Models (RSM) for anisotropy or LES/DES for higher-fidelity
10
* An explanation of the turbulent round jet/plane jet anomaly, S. Pope, 1978

## Slide 11: Thank you for your attention !
11

## Slide 12
12